## Slide 1
TableMate
Auditable bimanual manipulation in simulation
A reproducible MuJoCo workstation for two SO-101 arms
AI Infra Summit Hackathon | Online track | September 2026

## Slide 2
THE PROBLEM
A dinner instruction becomes inspectable action
Robotic table setting fails silently when perception, contact, and coordination are hidden.
TableMate keeps each decision and physical consequence visible: camera observations enter a planner, a supervisor selects a bounded skill, and MuJoCo verifies contacts and limits.
Operator needs
Fresh camera state
Task progress and stop control
Replayable evidence after every attempt

## Slide 3
ARCHITECTURE
A layered system with clear ownership
Instruction + cameras
Vision-language planner
Task supervisor
ACT skill policy
Contact and action checks
MuJoCo: two SO-101 arms, drawer, utensils, plate, cup
The supervisor owns prerequisites, arm assignment, timeouts, cancellation, recovery, and the final success decision.

## Slide 4
WHAT WE BUILT
Physics is part of the evidence
Contact-based manipulation
Grasps and hand-offs use MuJoCo contacts. Objects are never teleported or welded to a gripper.
Bounded learned actions
LeRobot ACT predicts joint targets from camera images and robot observations. Invalid, stale, and out-of-range actions are rejected.
Reproducible operations
Versioned contracts, run manifests, dataset lineage, recovery limits, CLI workflows, FastAPI portal, and seven lessons.
Native execution
The local development path uses verified ARM64 Python and keeps CPU and MPS evidence separate.

## Slide 5
MEASURED RESULT
The system stopped safely when the policy was unsafe
Teacher foundation
A complete contact-based teacher layout passed with synchronized camera replay and physical checks.
Learned evaluation
The CPU ACT candidate completed 20,000 updates. During physical placement, the contact guard stopped at 2.537 mm workbench overlap after 381 autonomous actions.
Interpretation
The run is recorded as a failure. The guard did not silently claim completion. Five corrective teacher trajectories then passed and remain separately labeled as teacher data.

## Slide 6
NEXT STEPS
Reproduce the evidence, then extend the envelope
Run locally
scripts/bootstrap.sh
scripts/check.sh --render
open the portal and replay retained runs
Complete the release gate
Finish sealed export parity, retrain from a fresh declaration, evaluate held-out scenes, and execute the final benchmark on real Intel Core Ultra hardware.
Repository
github.com/lipengyuan1994/bimanual-robotic-manipulation
Public lessons: lipengyuan1994.github.io/bimanual-robotic-manipulation/